## Slide 1
ROOFTOP
SOLAR
POTENTIAL
Mapping of the
IIT Delhi Campus
B.Tech Project · Mid-term Review
Tejas Suresh Kamble
2023EE10974
Surbhi Rathore
2023EE11224
Prof. Yashasvi Bansal
Supervisor
DEPARTMENT OF ELECTRICAL ENGINEERING

## Slide 2
01 · THE PROBLEM
Many flat roofs on
campus carry no panels.
Nobody has measured what they could generate.
1
Find the roofs still unused
2
Measure what is genuinely usable
3
Estimate the electricity
4
Check the grid can absorb it
Along the way
we found something
in the Institute's
own data that
nobody had
noticed.

## Slide 3
02
The data behind the study
GIVEN TO US
31
solar meters,
read every day
January 2024 — April 2026
17,000 daily readings across two spreadsheets
97 typing errors found and corrected
COLLECTED BY US
Sunshine records
NASA POWER · PVGIS
Building outlines
OpenStreetMap
Satellite imagery
Esri World Imagery
Sun angles
for panel row spacing

## Slide 4
03 · THE METHOD
Nine parts, four complete
1
Choose the buildings
10 roofs picked from 200
2
Read the meter data
31 meters, 28 months
3
Collect sunshine data
two sources, cross-checked
4
Measure the roofs
traced by hand in QGIS
5
Machine learning
scale to the whole campus
6
Shadows
what each roof loses
7
Calculate electricity
and validate it
8
Grid impact
can the network take it
9
Report and costs
payback and ranking
complete
still to do

## Slide 5
PART 1
Choosing
the buildings
Downloaded every campus building outline
Removed the 29 roofs that already have panels
Checked the rest on foot
10
buildings selected
3 hostels · 4 academic · 2 labs · 1 workshop

## Slide 6
PART 2 · READING THE METER DATA
Four plants have
stopped generating.
₹13
LAKH
of electricity never generated
₹1 lakh still lost
every month
The readings were written down every single day throughout.
Nobody had subtracted one day from the next.
Rupee figures estimated from plant size and a provisional tariff; the outages themselves are certain.

## Slide 7
PART 3
Collecting the sunshine data
10%
disagreement between
the two sunshine sources
— almost all of it in winter.
We settled it with the campus's own meters.
Real generation tracks NASA almost exactly.
Trusting the standard tool would have made every figure about 10% too high.

## Slide 8
PART 4 · MEASURING THE ROOFS
2.2 MWp
could be installed across the ten roofs
— about three times the solar the campus already has.
FROM ROOF TO PANELS
WHAT EACH ROOF COULD CARRY

## Slide 9
PARTS 5 TO 9
What comes next
5
Machine
learning
Train a model to find roofs automatically, so the method scales from 10 buildings to all 200.
6
Shadows
How much sun each roof loses to neighbouring buildings and trees.
7
Electricity
Convert sunshine and roof area into units, checked against the working plants.
8
Grid
impact
Whether the 11 kV network can absorb it. Waiting on three Estate Office documents.
9
Report
and costs
Payback, cost per unit, and the ranked list of roofs worth doing first.

## Slide 10
Thank you
Questions welcome
4
plants found stopped
10
roofs measured
2.2 MWp
untapped potential